AERMACCHI MB339 vers. 2010

FOR 8/12 KG TURBNE

ARF VERSION

Dear Customer,Thank you for purchase our mb339 product

Following you can find greater information for build and fly his model. Before you get started building and setting-up your aircraft, please make sure you have read this

instruction manual, and understood it. If you have any questions, please don’t hesitate to contact us.

Liability Exclusion and Damages

You have acquired a kit, which can be assembled into a fully working R/C model when fitted out

with suitable accessories, as described in the instruction manual with the kit.

However, as manufacturers, we at C&C Models are not in a position to influence the way you

build and operate your model, and we have no control over the methods you use to install,

operate and maintain the radio control system components. For this reason we are obliged to

deny all liability for loss, damage or costs which are incurred due to the incompetent or incorrect

application and operation of our products, or which are connected with such operation in any

way. Unless otherwise prescribed by binding law, the obligation of our company

to pay compensation is excluded, regardless of the legal argument employed.

This applies to personal injury, death, damage to buildings, loss of turnover and business,

interruption of business or other direct and indirect consequent damages. In all circumstances

our total liability is limited to the amount which you actually paid for this model.

BY OPERATING THIS MODEL YOU ASSUME FULL RESPONSIBILITY FOR YOUR ACTIONS.

It is important to understand that C&C Models, is unable to monitor whether you

follow the instructions contained in this instruction manual regarding the construction, operation

and maintenance of the aircraft, nor whether you install and use the radio control system

correctly. For this reason we at C&C Models  are unable to guarantee, or provide, a

contractual agreement with any individual or company that the model you have made will

function correctly and safely. You, as operator of the model, must rely upon your own expertise

and judgement in acquiring and operating this model.

RETRACTS AND OLEO LEGS INSTALLATION

All wood support are installed from the factory. For use in a grass field we suggest to reinforce the retracts support with hard wood (please see photo1)

Photo 1

Photo 2

In the photo2 you can see the correct position of the oleo leg and retract in the wing. Please check

The air system and the movement some time before to fix all system.

Photo 3

To control the anterior leg we have predisposed the servo hole in the anterior wood plate and you need to install the two linkage as to show in the photo.If you use our landing set the steering servo is integrated in the leg(see photo below)

Photo4

Photo5

All cilynder in the main and nose doors come already installed from the factory,you need only to buy the electronic or mechanic valve to move it.

SERVO INSTALLATION

All the servo hole are predisposed from the factory. In the kit you will find all hardware necessary to install it.For the servos type we suggest to use:

Aileron  2x 5,5-6 kg

Flap 2x 12kg

Elevator 2x 6kg

Fin 6/8 kg

For the servos flap you can install it internal in the wings, and the linkage must be out from the trailing edge (Please see photo 7 and 8  ) or the linkage must be out from the hole already fitted from factory(Please see photo 6)

Photo6

Photo 7

Photo 8

Photo 9

Install the servos in the black plastic support included in the kit and after screw the servos in a cover(see photo 10 and 11)

Photo 10

Photo 11

Photo 12

For the extreme aerobatic fly you need more movement for the mobile parts so you must to sand it,

(Please see photo 12).

Fuel tank installation

Before to install the 2,5 lt tank ,please check it carefully,

You need to create the Hole for air Inlet in the upper position of the fuel tank (Photo15)

To fit the fuel tank in the fuselage you need to remove the wood plate, insert the tank in the fuselage in vertical position and rotate it.

Photo 13

Photo14

After  positioned the fuel tank you can re- insert the wood plate(photo 14)

Photo15

Inox thrust pipe

Screw the inox pipe to the two turbine support using the two strips included in the pipe,we suggest you to add another inox strip to reinforce the tube.

Photo16

Position the turbine to max forward position

Photo17

Photo18

Typical servo linkage installation

Photo19

Typical electronic and UAT installation in the support.

In order to don’t install lead in the nose to reach the correct cg position we suggest to install all the heavy component(es. Battery) to max forward possible.However 300/400 lead grams are normal.

CG

The CG is located at 12 cm from the leading edge (please see photo below),you can set it accordling to your flying mode.

MOVEMENT

NORMAL FLIGHT:

AILERON: 20 MM UP 20 MM DOWN

FLAP: 30 MM TAKE OFF 80 MM LANDING

ELEVATOR: 30 MM UP 20 MM DOWN

RUDDER: 30 MM LEFT 30 MM RIGHT

MOVEMENT

ACROBATIC FLIGHT:

AILERON: 30 MM UP 30 MM DOWN

FLAP: 30 MM TAKE OFF 80 MM LANDING

ELEVATOR: 35 MM UP 30 MM DOWN

RUDDER: 40 MM LEFT 40 MM RIGHT

Photo20

Photo 21

Accessories

The wings are predisposed to accept the underwing tank and support. You will find In the wings 4 holes how to screw the 4 tank support (please see photo21)

Optional  Cockpit kit

C&c models  www.cmodels.it    info@cmodels.it